## Slide 1
A team can have up to 4 members including the team leader. Add rows if necessary.
Team Details
Team Name:
SR. NO
ROLE
NAME
ACADEMIC YEAR
1
Team Leader
2
Member 1
3
Member 2
COLLEGE NAME
TEAM LEADER CONTACT NUMBER
TEAM LEADER EMAIL ADDRESS
The T Guys
Aryan Chourasia
3rd Year
Govinda Podder
3rd Year
Ashish Bajaj
3rd Year
Thapar Institute of Engineering and Technology, Patiala
+91 90073 95333
achourasia_be24@thapar.edu

## Slide 2
Problem Statement Addressed
DESCRIPTION / DETAILS
PS-02, Applied Materials - recover navigation drift for wafer inspection, from imagery alone.
Re-find a site: sharp reference (1 nm/px, 1 um) inside a wide scan (10 nm/px, 10 um); both 1000x1000.
Output: pixel centre (x, y); if several regions match, the one closest to the image centre.
The reference is only 1% of the wide image - naive template matching cannot even run.

## Slide 3
Proposed Solution - Describe your Idea/Solution/Prototype
SOLUTION DETAILS
Known 10x zoom gap: shrink the reference to a 100x100 stamp, then localise by correlation. Entry point infer.py: predict(reference_path, search_path) -> (x, y).
DriftFind (classical): FFT normalised cross-correlation + blur/rotation search + centre tie-break + sub-pixel. No GPU.
DriftMatchNet (learned): Siamese encoder, learned NCC, adaptive shrinkage, centre-point heatmap + offset. Trained on a UNION of two generators for cross-domain robustness.
DriftRoute (router): learned matcher with a classical fallback - the submission entry point.

## Slide 4
Innovation and Uniqueness
KEY INNOVATION
One nm layout sampled twice (1 & 10 nm/px): exact analytic labels, not a resize.
A router fusing classical + learned matching, validated on the organizers' own reference generator.
Union-of-generators training for cross-domain robustness; physics-cited augmentation.
COMPETITIVE ADVANTAGE
94.5% within 5 px on the official reference generator vs 75.5% ZNCC baseline (+19 points).
Robust across generators (trained on a union of two); 86% on the hardest heavy-noise set (+27 vs baseline 59%).
Matches the evaluator's predict(reference, search) interface; classical fallback runs anywhere.

## Slide 5
Impact and Benefits
Primary Impact
Sensor-less drift recovery: pure software on existing captures, no extra hardware.
Sustains wafer-inspection throughput and yield; validated on the official generator.
Quantifiable Outcomes
94.5% default / 86.0% noisy (within 5 px) on the official reference generator
+19 / +27 points over the official ZNCC baseline (75.5% / 59%)
~150-430 ms/pair; classical path GPU-free
Sub-pixel median error ~0.6 px

## Slide 6
Technology & Feasibility/Methodology Used
IMPLEMENTATION STRATEGY
infer.py: predict(reference_path, search_path) -> (x, y), prints x,y - runs under the evaluator's harness as-is.
NumPy / SciPy (classical, CPU) + PyTorch (learned matcher, 4 GB GPU).
Coarse-to-fine correlation; validated end-to-end on the official reference generator (~0.6 px).
Dataset generator, all 3 matchers, training and evaluation - built and verified.
Software Architecture
Hardware Components
Development Tools

## Slide 7
Research and References
Research Background & Methodology
Augmentation follows the NIST ARTIMAGEN SEM image-formation paradigm; edge/noise parameters measured on real IC-SEM imagery and cross-checked with published values.
Matching builds on FFT normalised cross-correlation and Siamese / centre-point localisation. Full 24-source ledger in the repository.
References & Citations
Lewis, J. P. - Fast Normalized Cross-Correlation. Vision Interface, 1995.
Cutler et al. - Line-edge roughness metrology. J. Micro/Nanopattern. Mater. Metrol. 20(1) 010901, 2021.
Center-Point Multimodal Template Matching w/ Adaptive Shrinkage Cross-Correlation. Remote Sensing 16(15):2831, 2024.